PhET Circuit Construction

Using PhET software for building circuits, constructs circuits using the following sketches and answer the questions regarding each circuit.

# Circuit A

Q1.  Find the value of the current in the above circuit.		0.9A

# Circuit B

Q1.  Find the value of the current in the above circuit.		0.76A

Q2.  Calculate total resistance.					26.25Ω

Q3.  Find voltage across globe X					7.62V

Q4.  Find voltage across globe Y					12.38V

# Circuit C

Q1.  Find the value of the current in the above circuit.		0.42A

Q2.  Calculate total resistance.					62.34Ω

Q3.  Find the voltage across globe X					4.64V

Q4.  Find the voltage across globe Y					9.03V

Q5.  Find the voltage across the resistor				12.21V

# Circuit D

Q1.  Find the value of the current in the above circuit.		1.9A

Q2.  Calculate total resistance.					44.67Ω

Q3.  Find voltage across globe V					49.48V

Q4.  Find voltage across globe Y					12.69V

# Text boxes

9v

10Ω

20v

16.25Ω

10Ω

X

Y

29.4Ω

25.88V

21.76Ω

11.18Ω

Y

X

W

V

85V

26Ω

12Ω

X

10Ω

20Ω

Y